## Slide 1: Numerical Modelling in Geosciences

## Slide 2: Why numerical modelling in geosciences?
1. Most of the geological processes occur at timescales and depths such that they cannot be observed directly.
Accessible by drilling (max 10 km)
Unaccessible
Max. human timescale

## Slide 3: Why numerical modelling in geosciences?
2. Direct measurements of, for example, stress, deformation (strain rate), composition, temperature, pressure, etc., are limited to few rock samples. With numerical models we can know their distribution everywhere in our computational domain.

## Slide 4: Why numerical modelling in geosciences?
Field and geophysical data
Analogue/numerical modeling
Understanding geological processes
Lab. analysis/experiments and theory | 
3. Numerical modelling is an indispensable tool to understand the evolution of complex geological systems together with laboratory experiments (input) and field and geophysical observations (output).

## Slide 5: What is numerical modelling in geosciences?
To close the system we need rock physical properties from lab. experiments:
density
thermal conductivity, expansivity
heat capacity
rock mechanical properties
melting/metamorphic reactions
Discretization: FD,FE,FV
Eulerian+Lagrangian meshes
Conservation of momentum for slowly flowing continuous media
Conservation of energy
Fundamental PDEs in this course
P
Dt
c DT    q→  H
Conservation of mass for incompressible media
   P  g
  v  0

## Slide 6: Visualization is important!
Noble dame, 1959
© Succession Picasso / VG Bild-Kunst, Bonn 2
Sibylla von Cleve als Braut, Lukas Cranach d. Ä. (1472-1553)

## Slide 7
3 9.00E+03 0.00E+00 1.10E-09 -1.69E-09 0 196 1157 1.00E+19 3.00E-05 2.98E+02 0.00E+00 1.0
3 9.00E+03 0.00E+00 1.10E-09 -1.49E-09 0 227 1188 1.00E+19 3.00E-05 2.98E+02 0.00E+00 1.0
3 9.00E+03 0.00E+00 1.10E-09 -1.29E-09 0 258 1219 1.00E+19 3.00E-05 2.98E+02 0.00E+00 1.0
3 9.00E+03 0.00E+00 1.10E-09 -1.10E-09 0 289 1250 1.00E+19 3.00E-05 2.98E+02 0.00E+00 1.0
6.00E+0 | Numerical modeling without visualization |  |  |  |  |  |  |  |  |  |  |  |  | 0E+03
7.00E+0 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0E+03
8.00E+0 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0E+03
9.00E+0 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0E+03
1.00E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -8.96E-10 | 0 | 320 | 1281 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
1.10E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -6.97E-10 | 0 | 351 | 1312 | 1.00E+19 | 3.00E-05 | 3.15E+02 | 0.00E+00 | 1.00E+03 | 
1.20E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -4.98E-10 | 0 | 382 | 1343 | 1.00E+19 | 3.01E-05 | 3.81E+02 | 0.00E+00 | 1.00E+03 | 
1.30E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -2.99E-10 | 0 | 413 | 1374 | 1.00E+19 | 3.01E-05 | 3.98E+02 | 0.00E+00 | 1.00E+03 | 
1.40E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -9.96E-11 | 0 | 444 | 1405 | 1.00E+19 | 3.01E-05 | 3.98E+02 | 0.00E+00 | 1.00E+03 | 
1.50E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 9.96E-11 | 0 | 475 | 1436 | 1.00E+19 | 3.01E-05 | 3.98E+02 | 0.00E+00 | 1.00E+03 | 
1.60E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 2.99E-10 | 0 | 506 | 1467 | 1.00E+19 | 3.01E-05 | 3.98E+02 | 0.00E+00 | 1.00E+03 | 
1.70E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 4.98E-10 | 0 | 537 | 1498 | 1.00E+19 | 3.01E-05 | 3.98E+02 | 0.00E+00 | 1.00E+03 | 
1.80E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 6.97E-10 | 0 | 568 | 1529 | 1.00E+19 | 3.01E-05 | 3.81E+02 | 0.00E+00 | 1.00E+03 | 
1.90E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 8.96E-10 | 0 | 599 | 1560 | 1.00E+19 | 3.00E-05 | 3.15E+02 | 0.00E+00 | 1.00E+03 | 
2.00E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 1.10E-09 | 0 | 630 | 1591 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
2.10E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 1.29E-09 | 0 | 661 | 1622 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
2.20E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 1.49E-09 | 0 | 692 | 1653 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
2.30E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 1.69E-09 | 0 | 723 | 1684 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
2.40E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 1.89E-09 | 0 | 754 | 1715 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
2.50E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 2.09E-09 | 0 | 785 | 1746 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
2.60E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 2.29E-09 | 0 | 816 | 1777 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
2.70E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 2.49E-09 | 0 | 847 | 1808 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
2.80E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 2.69E-09 | 0 | 878 | 1839 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
2.90E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 2.89E-09 | 0 | 909 | 1870 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
3.00E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 0.00E+00 | 0 | 940 | 1901 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 2.02E+03 | 1.00E+03 | 
0.00E+00 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -2.89E-09 | 0 | 10 | 971 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 1.99E+03 | 1.00E+03 | 
1.00E+03 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -2.69E-09 | 0 | 41 | 1002 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
2.00E+03 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -2.49E-09 | 0 | 72 | 1033 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
3.00E+03 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -2.29E-09 | 0 | 103 | 1064 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
4.00E+03 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -2.09E-09 | 0 | 134 | 1095 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
5.00E+03 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -1.89E-09 | 0 | 165 | 1126 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
6.00E+03 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -1.69E-09 | 0 | 196 | 1157 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
7.00E+03 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -1.49E-09 | 0 | 227 | 1188 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
8.00E+03 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -1.29E-09 | 0 | 258 | 1219 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
9.00E+03 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -1.10E-09 | 0 | 289 | 1250 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
1.00E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -8.96E-10 | 0 | 320 | 1281 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 
1.10E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -6.97E-10 | 0 | 351 | 1312 | 1.00E+19 | 3.00E-05 | 3.15E+02 | 0.00E+00 | 1.00E+03 | 
1.20E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -4.98E-10 | 0 | 382 | 1343 | 1.00E+19 | 3.01E-05 | 3.81E+02 | 0.00E+00 | 1.00E+03 | 
1.30E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -2.99E-10 | 0 | 413 | 1374 | 1.00E+19 | 3.01E-05 | 3.98E+02 | 0.00E+00 | 1.00E+03 | 
1.40E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | -9.96E-11 | 0 | 444 | 1405 | 1.00E+19 | 3.01E-05 | 3.98E+02 | 0.00E+00 | 1.00E+03 | 
1.50E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 9.96E-11 | 0 | 475 | 1436 | 1.00E+19 | 3.01E-05 | 3.98E+02 | 0.00E+00 | 1.00E+03 | 
1.60E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 2.99E-10 | 0 | 506 | 1467 | 1.00E+19 | 3.01E-05 | 3.98E+02 | 0.00E+00 | 1.00E+03 | 
1.70E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 4.98E-10 | 0 | 537 | 1498 | 1.00E+19 | 3.01E-05 | 3.98E+02 | 0.00E+00 | 1.00E+03 | 
1.80E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 6.97E-10 | 0 | 568 | 1529 | 1.00E+19 | 3.01E-05 | 3.81E+02 | 0.00E+00 | 1.00E+03 | 
1.90E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 8.96E-10 | 0 | 599 | 1560 | 1.00E+19 | 3.00E-05 | 3.15E+02 | 0.00E+00 | 1.00E+03 | 
2.00E+04 |  | 9.00E+03 | 0.00E+00 | 1.10E-09 | 1.10E-09 | 0 | 630 | 1591 | 1.00E+19 | 3.00E-05 | 2.98E+02 | 0.00E+00 | 1.00E+03 | 

## Slide 8: Numerical modeling with visualization
400oC
800oC
1200oC
200oC
400oC
600oC
800oC
1000oC
1200oC
Temperature
Bulk Strain
Viscosity

## Slide 9: Computational resources
FERMI at CINECA, Bologna, Italy
This is not a coffee vending machine!
1D/2D models:
computation and visualization can be mostly done on local machines with moderate to high RAM and 1 to 8 CPUs (depending on the numerical resolution = problem size)(€ 1.500-4.000)
Workstation
3D models:
computation on supercomputing clusters (e.g., PLX, EURORA and FERMI at CINECA, Italy) with 100s to 1.000.000s CPUs. If many users, “problems” may arise due to long queuing times.
alternatively, with about € 100.000 it is possible to buy medium
size clusters (e.g., 384-786 CPUs) that could serve the whole department.
visualization requires powerful GPUs (€ 2.000-10.0000) and can be done on local machines or remotely using cluster’s GPUs.
Programming languages:
C/C++, Fortran, MatLab (€ 500-1000  Octave for free!)
Visualization softwares:
MatLab, Paraview, Amira,
etc.

## Slide 10: Computational Science?
Notes: Science?
Computational Science is a multidisciplinary activity, brings together people from a variety of disciplines.

## Slide 11: Computational Science
Complements, but does not replace, theory and experimentation in scientific research.
Experiment
Computation
Theory
Notes: Validation

## Slide 12: Computational Science
Has emerged as a powerful, indispensable tool for studying a variety of problems in scientific research, product and process development, and manufacturing.
Seismology
Climate modeling
Economics
Environment
Material research
Drug design
Manufacturing
Medicine
Biology
Analyze - Predict
Notes: Seismology: oil exploration, earthquake prediction (Parallel computation reduced compute time from weeks to hours)
Global ocean/ climate modeling: global warming, weather prediction
Economics: growth of a local or national economy (Agent-based modeling), management of resources, analysis of tax strategies
Environmental: utilization of resources, population modeling, insect control
Materials research: design of new materials, smart materials; shape driven by temperature materials; materials aging issues (Stockpile stewardship)
Drug design: design of anti-cancer drugs, etc.
Manufacturing: optimization of manufacturing processes, automation
Medicine: Medical imaging, MRIs
Human genome: applications to understanding and treating disease

## Slide 13: Example: Industry 
First jetliner to be digitally designed, "pre-assembled" on computer, eliminating need for costly, full-scale mockup.
Computational modeling improved the quality of work and reduced changes, errors, and rework.
www.boeing.com/commercial/
777family/index.html
Notes: !00% digitally designed using 3D computer graphics.
Bottom line: Reduced cost/Reduced time to market.

## Slide 14: Computational Science Process

## Slide 15: Mathematics
First of all: it is simple!!! First and second order derivatives.
(Very short) review of the mathematical background needed in this course to
handle partial differential equations (PDE): differential equations in which an unknown function is a function of multiple (rather than single) independent variables (space coordinates and time).
Example: 3D Heat diffusion equation 
In this course we will use the finite difference method to operate differentiation and numerically solve for PDEs
 k
2
 
x y2 z2


T 2T 2T 2T 
t



## Slide 16: Finite difference method
First derivative of function f(x) (1D case): f x f x  x  f x f x   lim x x0 (x  x)  x Analytical vs Numerical | Example: T  T  T2  T1 x x x2  x1 T  T   T2 1  x  x x1 x2 Δx
 | The same is valid for first derivative in time: T T T tt  T t   t t t

## Slide 17: Chapter Objectives
Understanding the meaning of local and global truncation errors and their relationship to step size for one-step methods for solving ODEs.
Knowing how to implement the following Runge-Kutta (RK) methods for a single ODE:
  Euler
  Heun
  Midpoint
  Fourth-Order RK
Knowing how to iterate the corrector of Heun’s method.
Knowing how to implement the following Runge-Kutta methods for systems of ODEs:
  Euler
  Fourth-order RK

## Slide 18: Ordinary Differential Equations
Methods described here are for solving differential equations of the form:
The methods in this chapter are all one-step methods and have the general format: where  is called an increment function, and is used to extrapolate from an old value yi to a new value yi+1.

## Slide 19: Euler’s Method
The first derivative provides a direct estimate of the slope at ti: and the Euler method uses that estimate as the increment function:

## Slide 20: Error Analysis for Euler’s Method
The numerical solution of ODEs involves two types of error:
  Truncation errors, caused by the nature of the techniques employed
  Roundoff errors, caused by the limited numbers of significant digits that can be retained
The total, or global truncation error can be further split into:
  local truncation error that results from an application method in question over a single step, and
  propagated truncation error that results from the approximations produced during previous steps.

## Slide 21: Error Analysis for Euler’s Method
The local truncation error for Euler’s method is O(h2) and proportional to the derivative of f(t,y) while the global truncation error is O(h).
This means:
  The global error can be reduced by decreasing the step size, and
  Euler’s method will provide error-free predictions if the underlying function is linear.
Euler’s method is conditionally stable, depending on the size of h.

## Slide 22: Runge-Kutta Methods
Runge-Kutta (RK) methods achieve the accuracy of a Taylor series approach without requiring the calculation of higher derivatives.
For RK methods, the increment function  can be generally written as: where the a’s are constants and the k’s are
where the p’s and q’s are constants.

## Slide 23: Classical Fourth-Order Runge-Kutta Method
The most popular RK methods are fourth-order, and the most commonly used form is: where:

## Slide 24: Systems of Equations
Many practical problems require the solution of a system of equations:
The solution of such a system requires that n initial conditions be known at the starting value of t.

## Slide 25: Solution Methods
Single-equation methods can be used to solve systems of ODE’s as well; for example, Euler’s method can be used on systems of equations - the one-step method is applied for every equation at each step before proceeding to the next step.
Fourth-order Runge-Kutta methods can also be used, but care must be taken in calculating the k’s.

## Slide 26: Solving Differential Equations Numerically
Example equation:
dy/dx + 2y = 1.3 e^{-x}
Initial condition:
y(0) = 5
Rewrite:
dy/dx = 1.3 e^{-x} - 2y
Goal: compute y(x) numerically.

## Slide 27: Why Numerical Methods?
Many differential equations cannot be solved analytically.
Example idea (Euler method):
y_{n+1} = y_n + h f(x_n, y_n)
But Euler can be inaccurate.
Runge–Kutta methods improve accuracy using several slope evaluations.

## Slide 28: Runge–Kutta 4 Method
Compute four slopes:
k1 = f(x_n, y_n)
k2 = f(x_n + h/2, y_n + h k1/2)
k3 = f(x_n + h/2, y_n + h k2/2)
k4 = f(x_n + h, y_n + h k3)
Update:
y_{n+1} = y_n + h/6 (k1 + 2k2 + 2k3 + k4)

## Slide 29: Example Step (RK4)
Equation:
f(x,y) = 1.3 e^{-x} - 2y
Initial values:
x0 = 0
y0 = 5
Step size:
h = 0.1
Compute slopes k1, k2, k3, k4.

## Slide 30: Result of RK4 Step
k1 = -8.7
k2 ≈ -7.893
k3 ≈ -7.974
k4 ≈ -7.229
Update:
y1 = y0 + h/6 (k1 + 2k2 + 2k3 + k4)
Result:
y(0.1) ≈ 4.206

## Slide 31: Geometric Interpretation
RK4 evaluates slopes at:
• start of the interval
• middle (twice)
• end of the interval
Weighted average of slopes:
k1 + 2k2 + 2k3 + k4
This gives a much more accurate estimate than Euler's method.